## Slide 1: Efficient Acoustic Modelling of Large Spaces Using Time Domain Methods
Work So Far

## Slide 2: What we will cover
Context
Plan
Validation
Work So Far
  Finite Difference Time Domain
  Pseudo Spectral Time Domain
  Sparse Finite Difference Time Domain
Next Steps
Code Review [optional]

## Slide 3: Context
Acoustic modelling is continually being applied to larger and more varied use cases e.g:
  Video Game Auralization
  Virtual Reality Auralization
  Scientific Simulation
  Cinematography
  Architectural Design
  Loudspeaker System Engineering

## Slide 4: Context
Time domain numerical methods may be optimised to provide:
  Appropriately accurate results for auralization applications
    [eventually in real time]
  Results for arbitrary and dynamic numbers of sources and receivers without fundamentally changing the calculation
  Impulse responses or signal data without significant changes in kernel equation i.e. flexible code
Time domain numerical methods have a few issues:
Require a significant number of calculations per time step
  Exponentially more with frequency
Explicit Euler methods have relatively high error
Applying these methods to very large simulations may not allow for feasible calculation times
The amount of memory required for large simulations may be implausibly large
Computing speed and power continues to increase, allowing time domain numerical methods to be a more realistic option

## Slide 5: Context
Develop and explore three numerical methods for acoustic simulation
  The Finite Different Time Domain Method
  The Pseudo-spectral Time Domain Method
  The Sparse Finite Difference Time Domain Method
Bench mark all three methods and compare execution time for a small domain
Bench mark all three domains and compare execution time for a very large domain
If successful, apply parallel processing to each algorithm and compare benchmarks
Document study
The aim of this study is to:

## Slide 6: Plan
Kernel Prototype
Test
Partially Absorbing Boundary Development
Sub-validate
Domain Instantiation
FDTD
1D
sub-validate
2D
sub-validate
3D
Validate
PSTD
1D
sub-validate
2D
sub-validate
3D
Validate
SFDTD
1D
sub-validate
2D
sub-validate
3D
Validate
Benchmark
Optimize / Validate
Benchmark / Document

## Slide 7: Validation
1D
  34m domain excluding boundaries
  ‘Time of flight’ 1mS
  Boundary absorption
    1 = pass-through [0dB across grid after 1ms + source prop time ]
    0 = perfect reflection [0dB of aggregate loss after source prop for 1s sim time]
  Sim must be stable up to 48kHz
2D
  10m * 10m domain
  ‘Time of flight’ to multiple receivers
  Receivers in line, peak level should reduce following inverse square law
  Sim must be stable up to 48kHz
3D
  5m * 4m * 3m domain
  ‘Time of flight’ should be concurrent with 2D and speed of sound
  Peak of receivers should match inverse square law
  Sim must be stable up to 48kHz
  Impulse response must cross-correlate with image source model to higher than 0.5 coefficient
    Spectral shifting is expected due to soft source implementation

## Slide 8: Benchmarking
Small Domain
  34m domain excluding boundaries
  ‘Time of flight’ 1mS
  Boundary absorption
    1 = pass-through [0dB across grid after 1ms + source prop time ]
    0 = perfect reflection [0dB of aggregate loss after source prop for 1s sim time]
  Sim must be stable up to 48kHz
Large Domain
  10m * 10m domain
  ‘Time of flight’ to multiple receivers
  Receivers in line, peak level should reduce following inverse square law
  Sim must be stable up to 48kHz

## Slide 9: Finite Difference Time Domain
Description
Staggered grid constitutive relation
  Pressure
  Velocity
Linearized Navier-Stokes Approximation
Forward Euler method
2nd order in space
2nd order in time
Requires 6~10 points per wavelength
Explicit
Local differentiation of finite points in space
Marching forward in half steps of time

## Slide 10: Finite Difference Time Domain
1D
  Kernel - Complete
  Absorbing Boundaries – Complete
  Sub-validation - Complete
2D
  Kernel - Complete
  Absorbing Boundaries – Complete
  Sub-validation – Incomplete
3D
  Kernel - Complete
  Absorbing Boundaries – Complete
  Sub-validation – Incomplete
Validation - Incomplete

## Slide 11: Pseudo-spectral Time Domain
Description
Uniform grid locations
Differentiation occurs in frequency domain
Differentiation across number of points in dimension
Error of order 2^NlogN
2nd order in time
Obeys Nyquist sampling theorem
  2 points per wavelength minimum
Marching forward in half steps of time

## Slide 12: Pseudo Spectral Time Domain
Example Code

## Slide 13: Pseudo Spectral Time Domain
1D
  Kernel - Complete
  Absorbing Boundaries – Complete
  Sub-validation - Incomplete
2D
  Kernel - Incomplete
  Absorbing Boundaries – Incomplete
  Sub-validation – Incomplete
3D
  Kernel - Incomplete
  Absorbing Boundaries – Incomplete
  Sub-validation - Incomplete
1D
  May require filtering the domain at each step to accommodate for high frequency aliasing due to non-smooth boundaries
2D
  Currently Unstable, due to PML
3D
  Waiting for further completing of 2D

## Slide 14: Sparse Finite Difference Time Domain
Description
Similar solving to FDTD
Solves local points where energy is above a threshold
Indexing function to determine points to be solved
Differentiation across number of points in dimension
May improve solving speed when the number of operations performed is less than the number of active grid points
May only improve performance when the dynamic range of the simulation is quite high

## Slide 15: Sparse Finite Difference Time Domain
0 pad ends of the domain
Decimate domain
Normalise values by threshold
Floor matrix
Reduce values above 1 to 1
Interpolate grid back to correct size
Ceil matrix

## Slide 16: Sparse Finite Difference Time Domain
1D
  Kernel – In Progress
  Absorbing Boundaries – Complete
  Sub-validation - Incomplete
2D
  Kernel - Complete
  Absorbing Boundaries – Complete
  Sub-validation – Incomplete
3D
  Kernel – In Progress
  Absorbing Boundaries – Complete
  Sub-validation - Incomplete
1D
  Window function is not smoothing enough- making the simulation unstable
2D
  Further confirmation of numerical dispersion not oscillating required, but looks promising
3D
  Yet to generate stable solving kernel, but work is in progress

## Slide 17: Next Steps
Fault find 1D SFDTD windowing algorithm
  More points
  Interpolate first?
Experiment with SFDTD noise floor
Get 3D SFDTD working
Fault find PSTD1D
  Why is the wave propagating 20 times slower?
Get 2D and 3D PSTD working
Create validation info from Image-Source program
Record validation results of FDTD 2nd order in all three dimensions
Optimisation [GPGPU]
Implement 4th order FDTD [nice to have]
Continue to write report / Documentation

## Slide 18: Code Review
[optional]